# PSG6&9Voices Card for HITACHI BASIC MASTER LEVEL3
Designed by Sasaji 2021 Rev. 0.2
 This is an extension card for HITACHI BASIC MASTER LEVEL3, markII and mark5. This is equipped with 3 PSGs and you can play with up to 9 voices.

Implementation

Installation

This card has two modes to control PSG via PIA and to do it via VIA.
PIA mode	This control two PSGs. You can play up to 6 voices. / Supported games: / Destroy Alien, The Cockpit
VIA mode	This control three PSGs. You can play up to 9 voices. / Supported games: / Skipper

You can toggle these modes using a I/O port by software, or buttons on the back side.

When specify from BASIC: / PIA: POKE &HFF34,0 / VIA: POKE &HFF34,&H81

# I/O Ports
PIA Register
Address	D7	D6	D5	D4	D3	D2	D1	D0	R/W
$FF30	DA7	DA6	DA5	DA4	DA3	DA2	DA1	DA0	R/W	PIA Data Register A / Write to PSG
$FF31									R/W	PIA Control Register A
$FF32	x	x	x	x	x	SEL	BDIR	BC1	R/W	PIA Data Register B / PSG Bus Control
$FF33									R/W	PIA Control Register B

When BDIR = 1 and BC1 = 1, latch register number on PSG.
When BDIR = 1 and BC1 = 0, write data to PSG.
When BDIR = 0 and BC1 = 1, read data from PSG.
SEL : Select PSG1 = 0, Select PSG2 = 1

PIA/VIA Select
Address	D7	D6	D5	D4	D3	D2	D1	D0	R/W
$FF34 / ($FF35)	CLK	x	x	x	x	x	x	V/P	R/W

V/P … “0”:Select PIA, “1”:Select VIA
CLK … Select clock on PSG “0”: 1MHz “1”:2MHz

VIA Register
Address	D7	D6	D5	D4	D3	D2	D1	D0	R/W
$FF70	x	x	x	PSG3	PSG2	PSG1	BC1	BDIR	R/W	ORB / PSG Bus Control
$FF71	DA7	DA6	DA5	DA4	DA3	DA2	DA1	DA0	R/W	ORA / Write to PSG
$FF72 / ~ / $FF7F										VIA Register / See datasheet of VIA for details.

When BDIR = 1 and BC1 = 1, latch register number on PSG.
When BDIR = 1 and BC1 = 0, write data to PSG.
When BDIR = 0 and BC1 = 1, read data from PSG.
PSG1:Select PSG1=1
PSG2:Select PSG2=1
PSG3:Select PSG3=1

# Jumper Pin

This connect the interrupt signals from PIA and VIA to the CPU side.
Normally, short the IRQ side (1-2).

# The back cover Extended terminal
PIA select button
VIA select button
"H” level when PIA,
"L” level when VIA.
Sound volume
# Attention
- You cannot adjust the sound using the volume on the main board. Please use it on the back cover.
- The Kanji ROM card and VIA address are duplicated. When select the VIA side, don’t read from Kanji ROM or VIA port.
- This board is a prototype. No consideration is given to noise generated during use and deterioration over time.
## No warranty
　We are not responsible for any damage caused by this card.
　You use this card at your own risk.

## Web
This document and CAD data are opened on the web.
GitHub(https://github.com/bml3mk5/L3PSG6n9Voices)
or
http://s-sasaji.ddo.jp/bml3mk5/l3psg6n9.htm#board

Sasaji (sasaji@s-sasaji.ddo.jp)
http://s-sasaji.ddo.jp/bml3mk5/
(Twitter: https://twitter.com/bml3mk5)